## Slide 1: Computer Architecture (CS F342) Lab-5(b) General-purpose Pipelined based MIPS Microprocessor Design Using Verilog HDL Sem-I, AY-2022-23 Date: Oct. 18, 2022 Submission Date: Oct. 24, 2022: 3AM Marks: 6
BITS-Pilani Goa, India. Dept. of CSIS

## Slide 2: Intellectual Property Rights (IPR)
/*########################################################
Note: Please don’t upload the assignments, template file/solution and lab. manual on GitHub or others public repository.
Kindly remove them, if you have uploaded the previous assignments.
It violates the BITS’s Intellectual Property Rights (IPR).
********************************************************/

## Slide 3: Design the following modules in the given template
File Name | Module | Marks
Dff.v | Dff_Reg | 0.2
1bitReg.v | register1bit | 0.2
2bitsReg.v | register2bit | 0.2
5bitsReg.v | register5bit | 0.2
stageIF_ID_Regs.v | IF_ID | 0.2
stageID_EX_Regs.v | ID_EX | 1
stageEX_MEM_Regs.v | EX_MEM | 0.2
stageMEM_WB_Regs.v | MEM_WB | 0.2
controller.v | controlCircuit | 1
topModule.v | pipelinedDatapath | 2
testbench.v | testbench | 0.2
For attending the Lab-5(b) [attendance needs to be recorded] |  | 0.4

## Slide 4
Register File
aluCtrl[3:0]
IM
PC
1
0
clk
reset
Testbench
0
1
<< 2
aluOp_ID_EX [1:0]
EN
sign_ext
0
1
4
DM
0
1
IF_ID
ID_EX
EX_MEM
MEM_WB
1
pcIn
pcOut
pcOut
pc
pc
ir
pc_IF_ID
ir_IF_ID
regWrite_MEM_WB
ir_IF_ID [25:21]
ir_IF_ID [20:16]
regRs
regRt
result
destReg_MEM_WB
ir_IF_ID [15:0]
signExtOut
ir_IF_ID [20:16]
ir_IF_ID [15:11]
signExtOut_ID_EX
pc_ID_EX
+
+
rt_ID_EX
rd_ID_EX
regDest_ID_EX
destReg_EX_MEM
rt_rd_ex_mem_in
aluSrcB_ID_EX
regRt_ID_EX
signExtOut_ID_EX
aluIn2
zero
ALU
ALU_CU
aluOut
regRs_ID_EX
branchAddress_EX_MEM
branch_EX_MEM
aluOut_EX_MEM
memData_EX_MEM
memRead_EX_MEM
memWrite_EX_MEM
aluOut_MEM_WB
memData_MEM_WB
memOut
[5:0]
branchAddress_EX_MEM
result
branchAddress
ctrlckt
aluOp[1:0]
aluSrc
regWrite
branch
memWrite
memtoReg
memRead
regDest
ir_IF_ID[31:26]
regRt_ID_EX
zero_EX_MEM

## Slide 5: Output
1-st Fib
2-nd Fib
4-th Fib
5-th Fib
6-th Fib
3-rd Fib
Pls. understand the opcode and clock.
7-th Fib

## Slide 6: Pipelined CU & its control signals at different stages
Read Ch-4 COD by P&H
Instr | Execution/Address Calc stage control lines |  |  |  |  | Memory access stage control lines |  |  | Write-back control lines | 
Instr | Jump | RegDst | ALUOp1 | ALUOp0 | ALUSrc | Branch | MemRead | MemWrite | RegWrite | MemtoReg
R-format | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
lw | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
sw | 0 | x | 0 | 0 | 1 | 0 | 1 | 0 | 0 | x
bne | 0 | x | 0 | 1 | 0 | 1 | 0 | 0 | 0 | x

## Slide 7: ALU controls and functions
Read Ch-4, COD by P&H
ALU control lines | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | Set on less than
1100 | NOR

## Slide 8: How the ALU control bits are set depends on the ALUOp control bits and different function code for R-type instruction
Read Ch-4, COD by P&H
Opcode | ALUOp | Instr. operation | Funct field | Desired ALU action | ALU control input
LW | 00 | Load word | xxxxx | add | 0010
SW | 00 | Stored word | xxxxx | add | 0010
BNE | 01 | Branch not equal | xxxxx | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
R-type | 10 | subtract | 100010 | subtract | 0110
R-type | 10 | AND | 100100 | AND | 0000
R-type | 10 | OR | 100101 | OR | 0001
R-type | 10 | Set on less than | 101010 | Set on less than | 0111

## Slide 9: ALU control/operation
Read Ch-4, COD by P&H
ALUOp |  | Funct field |  |  |  |  |  | Operation
ALUOp1 | ALUOp0 | F5 | F4 | F3 | F2 | F1 | F0 | 
0 | 0 | X | X | X | X | X | X | 0010
X | 1 | X | X | X | X | X | X | 0110
1 | X | X | X | 0 | 0 | 0 | 0 | 0010
1 | X | X | X | 0 | 0 | 1 | 0 | 0110
1 | X | X | X | 0 | 1 | 0 | 0 | 0000
1 | X | X | X | 0 | 1 | 0 | 1 | 0001
1 | x | x | X | 1 | 0 | 1 | 0 | 0111

## Slide 10: Blocking vs. Nonblocking Assignment
Verilog supports two types of assignment within always blocks, with subtly different behaviours
Blocking assignment: evaluation and assignment are immediate
Nonblocking assignment: all assignments deferred until all right-hand sides have been evaluated (end of simulation timestep)
Sometimes, as above, both produce the same result. Sometimes, not!
always @ (a or b or c)
begin
x = a ¦ b; 1. Evaluate a ¦ b, assign result to x
y = a ^ b ^ c; 1. Evaluate a ^ b ^ c, assign result to y
z = b & ~c; 1. Evaluate b & (~c), assign result to z
end
always @ (a or b or c)
begin
x <= a ¦ b ; 1. Evaluate a ¦ b, but defer assignment result to x
y <= a ^ b ^ c ; 2. Evaluate a ^ b ^ c, but defer assignment result to y
z <= b & ~c ; 3. Evaluate b & (~c), but defer assignment result to z
end 4. Assign results to x, y and z

## Slide 11: Pipelined D-FFs
CLK
D
D
D
Q
Q
Q
in
out
q1
q2

## Slide 12: Pipelined D-FFs
CLK
D
D
D
Q
Q
Q
in
out
q1
q2
module pipelinedDffs(input clk, input reset, input in, output out);
wire q1, q2;
dff d0 (clk, reset, 1'd1, in, q1);
dff d1 (clk, reset, 1'd1, q1, q2);
dff d2 (clk, reset, 1'd1, q2, out);
endmodule
module dff(input clk, input reset, input en, input d, output reg q);
always @(posedge clk)
if (reset == 1'b0)
if (en == 1'b1)
q = d;
always @(reset)
if (reset == 1'b1)
q = 0;
endmodule
module pipelinedDffs_TB(); //Testbench
reg in, clk, reset;
wire out;
pipelinedDffs uut(clk, reset, in, out);
always
#5 clk = ~clk;
initial
begin
clk = 1;
reset = 1;
in = 0;
$dumpfile("pipelinedDffs.vcd");
$dumpvars(0, uut);
#10 reset = 0; in = 1;
#10 reset = 0; in = 0;
#10 reset = 0; in = 1;
#10 reset = 0; in = 0;
#100 $finish;
end
endmodule
???
D
1st posedge clk
out=q2=q1=in
2nd posedge clk
out=q2=q1
3rd posedge clk
out = q2 = q1 =in
CLK
D
Q
Q
in
q1
q2
out
???

## Slide 13: Pipelined D-FFs
CLK
D
D
D
Q
Q
Q
in
out
q1
q2
module pipelinedDffs(input clk, input reset, input in, output out);
wire q1, q2;
dff d0 (clk, reset, 1'd1, in, q1);
dff d1 (clk, reset, 1'd1, q1, q2);
dff d2 (clk, reset, 1'd1, q2, out);
endmodule
module dff(input clk, input reset, input en, input d, output reg q);
always @(posedge clk)
if (reset == 1'b0)
if (en == 1'b1)
q <= d;
always @(reset)
if (reset == 1'b1)
q <= 0;
endmodule
module pipelinedDffs_TB(); //Testbench
reg in, clk, reset;
wire out;
pipelinedDffs uut(clk, reset, in, out);
always
#5 clk = ~clk;
initial
begin
clk = 1;
reset = 1;
in = 0;
$dumpfile("pipelinedDffs.vcd");
$dumpvars(0, uut);
#10 reset = 0; in = 1;
#10 reset = 0; in = 0;
#10 reset = 0; in = 1;
#10 reset = 0; in = 0;
#100 $finish;
end
endmodule
D

## Slide 14: Comparison
q <= d
q = d